## Slide 1: ① Autonomous production management
사내한 (Restricted)
■ Autonomous production management - Development Items / Required Technologies / Technical Pain Points
- Objective : Establish an autonomous decision-making system that generates multi-perspective scenarios (Productivity / Inventory / BTO)
while reflecting dynamic constraints (Supply Chain / Labor / Process)
Layer | Development Items | Required Technologies - DS | Required Technologies - DX |  | Development Pain-point
Connectivity | [Real-time Status Integration] API integration for real-time line-specific process status (Cycle Time, defects, downtime)​ [Risk Data Collection] Real-time data crawling and integration of external supply ​chain risk and Progress status by node, such as supplier part shortage ​risks and logistics delays​ | Real time event streaming through Kafka​ IIoT: Data Ingestion from sensors, PLC, etc.​ Relational DB (postgres) for app data and factory historian e.g. issue tickets, repair ticket, inspection records. This should be common for all apps to allow app to have access to data from other apps​ Time-series DB (influx) to support massive data ingestion sensors and equipment readings​ Event streaming (kafka) for real time event and alerts​ NoSQL for unstructured data​ Data platform to enable ETL, analysis and development of data products​ MCP Server exposes tools, data, or capabilities that AI assistants can use. ​ MCP Gateway to bridge between AI agents and MCP servers​ |  |  | • Legacy equipment without digital outputs • Noisy data and unstructured supply chain data Establishing 100% connectivity to relevant equipment is a critical, on-going process that must be aggressively optimized: Need to set up a structured process as relevant equipment connection is not a one-off exercise Need to establish an efficient workflow to accelerate the establishment of connection to existing or new equipment Need to be able to monitor and tweak connectivity parameters (Integrity, Frequency and Latency) over time
Data | [Domain Knowledge Digitalization] Digitalizing rules for factory managers' tacit ​knowledge (know-how) , labor constraints (working hours, skill matrix), and ​process specifics (equipment constraints)​ ​ [Master Data Integration] Standardizing data formats across SCM (Supply Chain),​ WMS (Inventory), IQIS (Quality), and MES (Process)​ ​ [Safety monitoring and intelligence] Human robot collaboration working environment safety ​ | Need Data Platform to facilitate the creation of “data products” to enable daily advanced analytics, as well as advanced use-cases (AI/ML etc)​ SDM : Facility ​ SIM: Omniverse, OpenUSD, Metropolis​ Mobile robot telemetry​ Synthetic Data Generation – MLOps​ Data retention policy​ | [P01.1 Production/Quality Knowledge Graph] Unified System of Records and digitalizing rules for factory managers' tacit knowledge (know-how, labor constraints (working hours, skill matrix), and processes (equipment and system constraints)​ ​ [DT01 Digital Twin based on 4M1S Single Data Model] Full Virtual representation of physical asset, process and events with continuous update from real-world data​ Digital Model of 4M1S in factory replicating property, behavior and performance in real-world​ Enterprise level Master Data Management and Process standardization across value streams – Design, Production, Workforce, Supply Chain, Logistics, Quality, ​Maintenance and Factory Operations​ ​ [A73.3 Factory traffic] Use case for DT01 on traffic safety and work at height safety​ ​ [Synthetic Data Generation Pipeline] simulate production scenarios to overcome HMGICS's low-volume ML data problem.​ Ability to generate synthetic data for specific use case e.g. training for virtual verification​ ​ [Tacit Knowledge Capture Schema] - structured elicitation templates encoding operator heuristics into the KG​ |  | Data requirements: Latency: Real-time vs cold, Flow: one-way vs two-way and Breadth: across systems vs single system connectivity Manpower: Large manpower is required to connect develop & manage systems

## Slide 2: ① Autonomous production management
사내한 (Restricted)
■ Autonomous production management - Development Items / Required Technologies / Technical Pain Points
- Objective : Establish an autonomous decision-making system that generates multi-perspective scenarios (Productivity / Inventory / BTO)
while reflecting dynamic constraints (Supply Chain / Labor / Process)
Layer | Development Items | Required Technologies - DS | Required Technologies - DX |  | Development Pain-point
Decision | [Risk Predictive Analysis] Predictive analysis of expected part shortage timing for specific lines based on real-time inventory and supply chain data​ [Dynamic Resource Management] Manage real-time production CAPA by matching currently available manpower (labor) and equipment status​ [Orchestration AI Engine Develop.] Automatic micro- production planning at the​ sequence level, simulating human manager tacit knowledge judgements​ [What-if Scenario Generation] ​ Generating multiple alternatives based on objective functions:​ ① Productivity First : Maximizing UPH and equipment utilization​ ② Inventory Optimization : Minimizing finished goods/WIP storage costs​ ③ BTO Optimization : Prioritizing customer order On-Time In-Full (OTIF) delivery rate​ [Virtual Validation for Scenario] Pre-simulating line balancing, bottlenecks, and potential shortages by inputting the 3 AI-proposed scenarios into a digital twin​ [Decision Support UI] Developing a dashboard where managers can compare ​expected effects (KPI changes) by scenario and give final approval and decision​ | MES and ERP Integration ​ Worker Terminal Interface​ Kafka (Event Streaming)​ MCP Gateway ​ Edge Computing Nodes (Private 5G-connected)​ Digital Twin Integration - State Reader, Floor Topology​ Audit Log​ OPC UA/ MQTT Integration for equipment safety​ | [P01.2 Real-time Schedule and Operation Rate Integration] Manage production schedule and resources based on real-time data​ ​ [P01.3 Digital Twin Simulation] Simulate line balancing, bottlenecks, and potential shortages by inputting AI-generated scenarios into a virtual factory digital twin​ ​ [P01.4 AI-Assisted Troubleshoot and RCA with HITL]​ Guided troubleshooting and RCA investigation with support from human inputs and following steps defined by SMEs​ ​ [P01.5 Predictive Planning with HITL Audit and Override]​ Demand forecasting: to anticipate customer requirements.​ Capacity prediction: to estimate available workforce and equipment.​ Constraint-aware scheduling: that considers materials, labor, and machine availability.​ Inventory Optimization: Minimize finished goods/WIP storage costs​ BTO Optimization: Prioritize customer order On Time In Full (OTIF) delivery rate​ Managers can compare expected effects (KPI changes) by scenario. Governed approval UI for AI recommendations.​ Features required:​ Enterprise Knowledge Graph for Production/Quality​ Workforce Skill Matrix Service​ Synthetic Data Generation Pipeline​ Multi-Objective Optimization Agent (MOO)​ High-Fidelity Digital Twin Platform​ What-If Simulation Engine ​ Plan-vs-Actual Comparison Engine ​ Rollback Decision Logic Engine​ Deviation detection and alert​ RACS Integration​ Path planning and conflict resolution |  | • Technical load of reflecting constantly changing dynamic variables into the real-time analysis model without latency • High computational load of multi-objective optimization • Difficult to synchronize 100% the physical and virtual model without error • Interoperability of simulation systems and legacy systems

## Slide 3: ① Autonomous production management
사내한 (Restricted)
■ Autonomous production management - Development Items / Required Technologies / Technical Pain Points
- Objective : Establish an autonomous decision-making system that generates multi-perspective scenarios (Productivity / Inventory / BTO)
while reflecting dynamic constraints (Supply Chain / Labor / Process)
Layer | Development Items | Required Technologies - DS | Required Technologies - DX |  | Development Pain-point
Action | [Automated Work Dispatch] Automated transmission of updated production plan sequence and work instructions to PLCs and worker terminals based on the finalized scenario [Adaptive Logistics] Automated part delivery (JIS/JIT) and Logistic path optimization synchronized with updated production plan sequence [Digitalized Production Resource Plan] Build-to-order plan | MES and ERP Integration (2-way) Worker Terminal Interface Kafka (Event Streaming) MCP Gateway Edge Computing Nodes (Private 5G-connected) OPC UA/ MQTT Integration for equipment safety | [P01.7 Plan Execution Monitoring & Rollback] continuous plan-vs-actual comparison with automated rollback triggers; without this the action layer is open-loop [P01.6 Constraint-Aware Dispatch Engine] validates AI instructions against hard safety/capacity constraints before execution [P02.1 Operations Orchestrator] Manage real-time plan change by matching currently available workforce (labor) and equipment status. Make real-time seq adjustment to rebalance or debottleneck (Including long-term CM) (refine with autonomous execution – system/apps) HITL Authority Matrix Tiered Authority Model Rules Engine Digital Twin Integration - State Reader, Floor Topology Audit Log [A71.3 Sales to delivery reporting, Test car inventory management] provide visibility on vehicle status in factory from sales orders [A71.4 Worker Availability Management] provide visibility on worker availability by integrate SAP work order with worker attendance, and job allocation for NPI and other non-production [A71.5 Integrated resource management hub] integrated and change work order planning in SAP APS API integration SucessFactors data ingestion |  | • When the AI changes plans, control and physical control technologies are required to minimize lead time by re-routing in real time the work-in- process (WIP) already deployed on the line and logistics in transit.
Learning | [Expert Imitation Learning] Collecting history of managers overriding AI-established plans to retrain the AI on managers’ decision-making patterns (Behavioral Cloning) [Perform.-based Reward Learning] Automatically updating AI algorithm weightage by evaluating actual achievement rates (productivity, delivery compliance) against the plan [Explainable AI (XAI)] Generate explanations for people to gain trust and support of AI decisions made | • MLOps Pipelines: (continuous model deployment/Mgm.) • Hi-Fidelity Event Log: ‘Black Box’ recorder • State-Action mapping engines • Contextual Metadata Tagging | [P02.3 Self-Optimizing operation orchestrator] Self-learning and optimizing dynamic planning and orchestration [Imitation Learning] AI model training by mimicking actions of a human expert based on historical state-action pairs (Behavioral Cloning) or by learning from human feedback or overrides to refine AI decision-making (Human-in-the-Loop) [Outcome-based Reinforcement Learning] AI model training by performing actions and receiving rewards/penalties based on outcome against the plan [Explainable AI (XAI)] Generate explanations for people to gain trust and support of AI decisions made |  | • Decline in shop floor acceptance (Trust) that occurs when the AI cannot explain to field workers why it recommended a specific scenario (XAI limitation) : Need to learn logic applicable for communication with shop floor workers (e.g., new car events, process improvements)

## Slide 4: ① 생산 관리 자율화
사내한 (Restricted)
■ 생산 관리 자율화 - 개발 항목 / 필요 기술 / 극복 과제
계층 | 개발 항목 | 필요 기술 – DS | 필요 기술 – DX |  | 개발 Pain-point
연결 계층 (Connectivity) | [실시간 현황 연동] 라인별 실시간 공정 현황(C/T, 불량, 정지) API 연동 [리스크 데이터 수집] 협력사 부품 결품 위험, 물류 지연 등 외부 공급망 리스크 및 노드별 진행현황에 대해 데이터 실시간 크롤링 및 연동 | • IIoT Gateways: sensors, PLC, etc. • Time-series DBs: InfluxDB, etc. • EAI / ESB: Enterprise system integration • Web Scraping, API Aggregators, NLP • ETL pipelines & Semantic Middleware |  |  | • 실시간 라인 문제들은 사람이 아닌, 명확히 분류된 카테고리 에 얼라인된 알람으로 자동 수집되고 분석되어야 함. • 수많은 협력사의 공급망 데이터를 실시간 투명하게 확보 필요 (Vattz 시스템 활용 전 협력사 data 연계 필요)
데이터 계층 (Data) | [도메인 지식 데이터화] 공장 관리자의 암묵지(노하우), 노무 제약 (근로시간, 스킬 매트릭스), 공정 특이사항(설비 제약)의 룰 데이터화 [기준 정보 통합] SCM, WMS(재고), IQIS (품질) MES(공정) 데이터 포맷 표준화 | • MDM (Master Data Mgmt) • SDM (Single Data Model) & Data Catalogs • Workforce Skill Matrices • DataLake (Un/Structured data integration) • Big Data Analytics (Spark, etc.) |  |  | • 베테랑 관리자의 직관적 판단(암묵지)을 정량적 데이터와 알고리즘 룰로 변환하는 과정의 난해함 • 공장별 특이사항에 대한 조사 및 프로세스 표준화 고려 필요
의사결정 계층 (Decision) | [리스크 예측 분석] 실시간 재고 및 공급망 데이터를 바탕으로 특정 라인의 '결품 예상 시점' 사전 분석 [제약 조건 종합] 현재 가용한 인력(노무)과 설비 상태를 매칭하여 실시간 생산 가능 CAPA 산출 [오케스트레이션 AI 엔진 개발] 관리자 수준의 서열(Sequence) 단위 미세 생산 계획 자동 수립 알고리즘 개발 [다각적 시나리오 도출 로직] 목적 함수에 따른 복수 대안 생성 ① 생산성 우선: UPH 극대화 및 설비 가동률 중심 ② 재고 최적화 : 완성차/재공품(WIP) 보관 비용 최소화 ③ BTO 최적화: 고객 주문 납기 준수율(OTIF) 최우선 [시나리오 가상 검증] AI가 제안한 3가지 시나리오를 디지털 트윈에 입력하여 라인 밸런싱, 병목, 결품 여부 사전 시뮬레이션 [의사결정 지원 UI] 관리자가 시나리오별 기대 효과(KPI 변화)를 비교하고 최종 승인할 수 있는 대시보드 개발 | • Knowledge Graph & Rule Mgmt System • Next-gen SCM • Time-Series Foundation Models: (shortage/delay prediction) • Cloud-Scale Parallel Computing • CEP (Complex Event Processing) • Multi-Objective Optimization (MOO) Algorithms (MILP, heuristic optimization) • Agentic AI & LLM Reasoning • Reinforcement Learning (RL-based sequence optimization) • Scenario Planning Module • High-Fidelity Digital Twin Platform • What-If Analysis Dashboard |  |  | • 시시각각 변하는 동적 변수(갑작스러운 결근, 설비 고장, 부품 지연)를 실시간 분석 모델에 지연 없이 반영하는 기술적 부하 : 리던던시 고려한 안정적인 기본 룰베이스 운영 원칙과 연계 필요성 검증 • 상충 목표 (예: 생산 안정화 vs 재고 최소화) 사이에서 최적의 타협점(Trade-off)을 찾는 복합적인 의사결정 가능한 최적화 알고리즘의 높은 연산 복잡도 • 현실 라인의 물리적 제약 (컨베이어 속도, 버퍼 공간 등)을 가상 공간에 오차 없이 100% 동기화하는 모델링 어려움 : 과거 data 활용하여 순차적으로 오차 축소 가능 예상
조치 계층 (Action) | [라인별 지시 하달] 확정된 시나리오를 바탕으로 각 현장 라인의 PLC 및 작업자 단말기에 서열 지시서 자동 전송 [물류 동기화] 생산 서열에 맞춘 부품 불출(JIS/JIT) 및 AGV 이송 지시 자동화 | • Smart MES / WMS / Worker Terminals • Private 5G / Edge Computing • Smart Fleet Mgmt System & Navigation • RCS (Robot/AGV Control Systems) |  |  | • AI의 계획 변경 시, 이미 라인에 투입된 재공품(WIP)과 이동 중인 물류의 동선을 실시간으로 재조정 (Re-routing) 하여 리드타임을 최소화 하는 관제 및 물리적 제어 기술 필요
학습 계층 (Learning) | [전문가 모방 학습] AI가 수립한 계획을 관리자가 수정(Override)한 이력을 수집하여, 관리자의 의사결정 패턴을 AI에 재학습 [실적 기반 보상 학습] 계획 대비 실제 달성률(생산성, 납기 준수율)을 평가하여 AI 알고리즘의 가중치 자동 업데이트 [설명 가능한 AI(XAI)] AI의 결정에 대한 설명을 제공하여 사람들이 신뢰를 얻음 | • MLOps Pipelines: (continuous model deployment/Mgm.) • Hi-Fidelity Event Log: ‘Black Box’ recorder • State-Action mapping engines • Contextual Metadata Tagging • Attention and Saliency maps |  |  | • AI가 왜 특정 시나리오를 추천했는지 현장 작업자에게 설명(XAI)하지 못할 경우 발생하는 현장의 수용성 (Trust) 저하 문제 : 현장 작업자와 소통 가능한 논리 (신차 이벤트, 프로세스 개선 등) 학습 필요
- 목표 : 동적 제약 조건 (공급망 / 노무 / 공정) 을 실시간으로 반영하며, 다각적 관점 (생산성 / 재고 / BTO) 의 최적화 시나리오를 생성하는 자율 의사결정 체계 구축
Need to translate KR Ver later

## Slide 5: ② Autonomous parts supply and inventory mgmt
사내한 (Restricted)
■ Autonomous parts supply / inventory management - Development items / Required technologies / Technical pain points
- Objective : Establish end-to-end visibility from global suppliers (VDR) to final assembly line, and build an autonomous ordering
and inventory optimization system that accounts for logistic, and operational risks
Layer | Development Items | Required Technologies - DS | Required Technologies - DX |  | Development Pain-point
Connectivity | [End-to-End Supply Chain Data Connectivity] Integration of Tier 1 VDR production/inventory status and issues (fire, fatalities, labor disputes, etc.), and real-time location (GPS) tracking for vessel/air/inland transport. [Logistics Supply Delay Risk Data Collection] Collection of data on logistics supply delay risks caused by global wars, port strikes, extreme weather events, etc. [Intra-factory logistics Connectivity] Integration of logistics hardware within HMGICS to other logistics processes | [S/W] • EDI platforms for supplier inventory and order status visibility • S&OP solution for Planning, • Shipment cost and status tracking solutions • IIoT connectivity for logistics hardware | [End-to-End Supply Chain Connectivity] Inventory data across all locations within scope – Container Yard, Depot & HMGICS across all levels Inventory movement data from different legacy and ERP systems with no information leakages (including timestamps of transactions) Planning data – Demand & Supply plan, Production plan [Logistics Supply Delay Risk Data Collection] Procurement data – Supplier stock positions, PO quantities Logistics data – Inbound shipment tracking with delay alerts Logistics & Procurement cost benchmarks Parts QC data [Intra-factory logistics Connectivity] Connectivity of logistics process flow with hard |  | Data sharing (Visibility) avoidance by Tier 1due to lack of IT infrastructure and fear of trade secret leaks Cost of building and maintaining a real-time data network for each logistics node Limitations in real-time collection of unstructured data (news, policies)
Data | [Global Logsitics Control Tower Unified View] Definition of All Node / Data (transportation & Inventory): VDR Warehouse ➔ Port ➔ Ocean ➔ CC (Consolidation Center) ➔ Factory Warehouse ➔ Line-side [BOM-based Data Standardization] Mapping and standardizing different VDR part numbers into the internal OEM BOM (Bill of Materials) structure | Integrated logistics data warehouse – Planning, Inventory (end-to-end), orders, Transportation (Ocean, Air, Land), QC Records Single Data Model for end-to-end logistics Enterprise Knowledge Graph Supply Chain IIoT: Data Ingestion from sensors, PLC, etc. Connector and Data pipeline to systems/app DB: MES, IQIS, GPTIS, HALO Relational DB (postgres) for app data and factory historian e.g. issue tickets, repair ticket, inspection records. This should be common for all apps to allow app to have access to data from other apps Data platform to enable ETL, analysis and development of data products Need Data Platform to facilitate the creation of “data products” to enable daily advanced analytics, as well as advanced use-cases (AI/ML etc) MCP Server exposes tools, data, or capabilities that AI assistants can use. MCP Gateway to bridge between AI agents and MCP servers UNS for Digital Twin | [SX Supply Chain Knowledge Graph] Unified System of Records Integration of operational and planning data for (autonomous) planning Data integration across layers including tier 1 suppliers Integrate inventory data for autonomous ordering and planning [DT01 Digital Twin based on 4M1S Single Data Model] Full virtual representation of physical asset, process and events with continuous update from real-world data Digital Model of 4M1S in factory replicating property, behavior and performance Enterprise level Master Data Management and Process standardization across value streams – Design, Production, Workforce, Supply Chain, Logistics, Quality, Maintenance and Factory Operations |  | Participation required in VDR part data standardization (or automatic mapping) based on the global part data standardization policy

## Slide 6: ② Autonomous parts supply and inventory mgmt
사내한 (Restricted)
■ Autonomous parts supply / inventory management - Development items / Required technologies / Technical pain points
- Objective : Establish end-to-end visibility from global suppliers (VDR) to final assembly line, and build an autonomous ordering
and inventory optimization system that accounts for logistic, and operational risks
Layer | Development Items | Required Technologies - DS | Required Technologies - DX |  | Development Pain-point
Decision | [Risk-based Lead Time (L/T) Prediction] Calculating the probability of arrival delays and estimated lead time (L/T) for each part by analyzing risks such as transit time by transportation mode, weather, and strikes [Multi-Echelon Inventory Optimization (MEIO)] Autonomous calculation of optimal Safety Stock, Shortage Risk and Review of optimal order quantity at each logistics node [Autonomous Ordering & Sourcing Alternative Countermeasure] Calculating optimal additional order quantities and deriving alternative routing scenarios (e.g., switching from ocean to air freight) when shortages are expected [What-If Simulation] ex: Providing supply chain disruption simulations Considering global geopolitical risks, such as ‘the impact on the assembly line 3 weeks after the Suez Canal is blocked’ | ML Ops pipeline IIoT: Data Ingestion from sensors, PLC, etc. Connector and Data pipeline to systems/app DB: MES, IQIS, GWMS, GPTIS, HALO Relational DB (postgres) for app data and factory historian e.g. issue tickets, repair ticket, inspection records. This should be common for all apps to allow app to have access to data from other apps Data platform to enable ETL, analysis and development of data products Need Data Platform to facilitate the creation of “data products” to enable daily advanced analytics, as well as advanced use-cases (AI/ML etc) MCP Server exposes tools, data, or capabilities that AI assistants can use. MCP Gateway to bridge between AI agents and MCP servers Enterprise Knowledge Graph Supply Chain ERP Integration (SAP, Oracle, etc.) Multi-objective AI Agents for S&OP End-to-end inventory data orchestration Optimal ordering and PO automation Inventory inaccuracy tracking and adjustment workflow Order tracking and real-time replanning End-to-end planning vs. operations orchestration | [AI-enabled Lead Time (L/T) & Delay Prediction] Calculating the probability of arrival delays and estimated lead time (L/T) for each part by tracking supplier inventory analyzing risks such as transit time by transportation mode, weather, and strikes Predictive AI : Time-series based L/T delay prediction Cognitive AI : NLP-based risk analysis [What-If Simulation] End-to-end supply chain planning simulation + disruption-based alternative scenario planning (e.g. ‘the impact on the planned assembly due to supplier shortages or inbound delays) Digital Twin : Supply Chain Flow simulation |  | It is difficult to create a model that analyzes the impact of issues such as geopolitical risks or tariff wars on logistics supply. Controlling the Bullwhip Effect, where small forecast errors amplify across the entire supply chain
Action | [Autonomous Purchase Order (PO) Execution] Automatically issuing POs to VDRs by integrating AI-determined optimal order quantities with the ERP system [Dynamic Logistics Routing Instructions] Automatically issuing transport mode change instructions (Ocean ➔ Air) to the forwarder's system for urgent parts [Emergency In-house Logistics Deployment] Issuing urgent transfer instructions to AGVs/forklifts to immediately feed safety stock from the in-house warehouse to the line when a shortage is imminent [Logistics Supply Chain Transition] Proposing optimal alternatives (component VDRs, suppliers) to respond to global risk |  | [AI-enabled inaccuracies and obsolescence identification] Whenever parts inventory is inaccurate or parts are at the risk of obsolescence due to change in plan, automatically send alerts to the logistics [Autonomous order Execution] Automatically issuing POs by integrating inventory positions with optimal order quantities [AI-enabled Dynamic Logistics mode switching] Automatically issuing transport mode change instructions (Ocean ➔ Air) to the forwarder's system for urgent parts [AI-enabled end-to-end Supply Chain Orchestration] End-to-end real-time replanning based on decision agents considering chosen objective (cost, lead time, etc.) and current and future predicted disruptions |  | Issues of financial liability and delegation of authority when AI dictates autonomous orders worth billions or expensive air freight conversions Limitations in automatically reflecting contract terms (e.g., penalties) with VDRs and logistics companies

## Slide 7: ② Autonomous parts supply and inventory mgmt
사내한 (Restricted)
■ Autonomous parts supply / inventory management - Development items / Required technologies / Technical pain points
- Objective : Establish end-to-end visibility from global suppliers (VDR) to final assembly line, and build an autonomous ordering
and inventory optimization system that accounts for logistic, and operational risks
Layer | Development Items | Required Technologies - DS | Required Technologies - DX |  | Development Pain-point
Learning | [Inventory Optimization and Autonomous Ordering Automatic Update] Improving algorithms based on actual supply performance [Automatic VDR Reliability Index Update] AI automatically updates the 'Risk Score' (reliability weight) of specific VDRs or logistics routes by comparing planned L/T against actual arrival times [Black Swan Event Learning] Enhancing crisis response models by learning supply/demand fluctuation patterns during past supply chain disruptions (COVID-19, wars, etc.) | MLOps (Continuous monitoring and deployment of predictive models) Reinforcement Learning (planning optimization learning) | [Autonomous Ordering Automatic Update] Improving algorithms based on actual supply performance [Autonomous replanning based on performance] Improving Sales & Operations Planning algorithms based on actual historic performance [Automatic supplier reliability Index Update] AI automatically updates the 'Risk Score' (reliability weight) of suppliers or logistics routes by comparing planned L/T against actual arrival times |  | • Absolute lack of historical data for AI to learn from due to the low frequency of extreme crises (Black Swans) like wars and pandemics (Data Sparsity problem)

## Slide 8: ② 부품 공급 및 재고 관리 자율화
사내한 (Restricted)
■ 부품 공급 및 재고 관리 자율화 - 개발 항목 / 필요 기술 / 극복 과제
- 목표 : 글로벌 협력사 (VDR) 부터 최종 조립 라인까지의 End-to-End 가시성을 확보하고, 다양한 리스크 (물류적, 운영적) 를 종합적으로
반영하는 자율 발주 및 재고 최적화 체계 구축.
계층 | 개발 항목 | 필요 기술 – DS | 필요 기술 – DX |  | 개발 Pain-point
연결 계층 (Connectivity) | [End-to-End 공급망 데이터 연동] Tier 1 VDR의 생산/재고 현황 및 이슈 (화재, 사망,노사갈등 등), 선박/항공/내륙 운송 실시간 위치(GPS) 트래킹 연동 [물류 공급 지연 리스크 데이터 수집] 글로벌 전쟁, 항만 파업, 기상 이변 등 영향으로 인한 물류 공급 지연 리스크 데이터 수집 | • B2B EDI / API Gateway (협력사 연동) • IoT Tracking (컨테이너/팔레트 RFID, GPS) • Web Crawler & NLP (뉴스/시황 수집) |  |  | • Tier 1의 IT 인프라 부재 및 영업 기밀 유출 우려로 인한 데이터 공유(Visibility) 기피 현상 • 각 물류 노드별 데이터 실시간 연결망 구축 및 유지 비용 • 비정형 데이터(뉴스, 정책)의 실시간 수집 어려움
데이터 계층 (Data) | [글로벌 SCM 컨트롤 타워 통합 뷰 구축] VDR 창고 ➔ 항만 ➔ 해상 ➔ CC (통합물류센터) ➔ 공장 창고 ➔ 라인 까지의 전 노드(Node) / 데이터 정의[BOM 기반 데이터 표준화] 각기 다른 VDR의 부품 번호를 완성차 내부 BOM (자재명세서) 체계로 매핑 및 표준화 | • Supply Chain Control Tower Platform • MDM (Master Data Management - BOM/자재 기준정보) • Data Lakehouse (글로벌 데이터 통합) |  |  | • 글로벌 부품 데이터 표준화 정책 기반, VDR 부품 데이터 표준화 (혹은 자동 매핑) 참여 필요
의사결정 계층 (Decision) | [리스크 기반 리드타임 (L/T) 예측] 운송 방식별 소요 기간, 기상, 파업 등 리스크 분석하여 부품별 도착 지연 확률 및 예상 L/T 산출 [다단계 재고 최적화 (MEIO)] 각 물류 노드별 적정 안전 재고(Safety Stock) 자율 계산 및 결품 위험도 산출, 최적 발주량 검토 [자율 발주 및 소싱 대안 생성] 결품 예상 시, 최적의 추가 발주량 계산 및 대안 경로 (예: 해상 운송 ➔ 항공 운송 전환) 시나리오 도출 [What-If 시뮬레이션] 예 : 글로벌 물류 공급 리스크 고려 “수에즈 운하가 막혔을 때 3주 뒤 조립 라인에 미치는 영향" 등 공급망 단절 시뮬레이션 제공 | • Predictive AI : 시계열 기반 L/T 지연 예측 • Cognitive AI : 물류 공급 리스크 분석 • MEIO Solver : 다단계 재고 최적화 알고리즘 • Digital Twin : 공급망 네트워크 시뮬레이션 (Supply Chain Network Design) |  |  | • 지정학적 리스크나 관세 전쟁 같은 이슈에 따른 물류 공급 영향도를 분석하는 모델을 만드는 것은 난해함. • 작은 예측 오차가 공급망 전체로 증폭되는 채찍 효과 (Bullwhip Effect) 통제
조치 계층 (Action) | [자율 발주(PO) 실행] AI가 결정한 최적 발주량을 ERP 시스템과 연동하여 VDR에게 구매 주문서(PO) 자동 발행 [동적 물류 라우팅 지시] 긴급 부품에 대해 포워더 (물류사) 시스템에 운송 수단 변경 (해상➔항공) 지시 자동 하달 [사내 물류 긴급 투입] 결품 임박 시, 사내 창고의 안전 재고를 라인으로 즉시 투입하도록 AGV/지게차에 긴급 이송 지시 [물류 공급망 전환] 글로벌 리스크 대응 위한, 최적 대안 (부품 VDR, 공급사) 제안 | • ERP Integration (SAP, Oracle 등 연동) • RPA (Robotic Process Automation - 발주 자동화) • TMS (Transportation Management System) |  |  | • AI가 수십억 원 규모의 자율 발주나 값비싼 항공 운송 전환을 지시했을 때 발생하는 재무적 책임(Liability) 및 권한 위임 문제 • VDR 및 물류사와의 계약 조건(위약금 등) 자동 반영 한계
학습 계층 (Learning) | [재고 최적화 및 자율 발주 자동 업데이트] 실제 공급 실적 기준 알고리즘 개선 [VDR 신뢰도 지수 자동 업데이트] 계획된 L/T 대비 실제 도착 시간을 비교하여, 특정 VDR이나 물류 루트의 '신뢰도 가중치 (Risk Score)'를 AI가 자동 업데이트 [블랙스완 이벤트 학습] 과거의 공급망 붕괴 사례 (코로나19, 전쟁 등) 발생 시의 수요/ 공급 변동 패턴을 학습하여 위기 대응 모델 고도화 | • MLOps (예측 모델 지속 모니터링 및 배포) • Reinforcement Learning (재고 정책 최적화 학습) |  |  | • 전쟁, 팬데믹 같은 극단적 위기(Black Swan)는 발생 빈도가 낮아 AI가 학습할 과거 데이터가 절대적으로 부족함 (Data Sparsity 문제)
Need to translate KR Ver later

## Slide 9: ③ Autonomous robot teaching and calibration
사내한 (Restricted)
■ Autonomous robot teaching / calibration - Development items / Required technologies / Technical pain points
- Objective : Achieve a "Teaching-less" factory through Digital Twin-based Virtual Commissioning (Sim-to-Real) and establish
an autonomous system that compensates for micro-tolerances of car bodies, parts, and equipment in real-time using edge vision and sensors.
Layer | Development item | Required Skills – DS | Required Skills – Core R&D |  | Development Pain-point
Connectivity Layer | [Data Interface and System Integration] (Step 1) • Establish Main equipment connectivity system & field-virtual basic data linkage • Establish a manual and periodic data collection base for the site (Step 2) • Establish an automated data collection & connectivity system for site operations • Build a closed-loop linkage environment for mutual reflection of real-virtual data | [Integrated Connectivity Platform Technology] Upper System-Site Data Link Structure Technology (Aligned with ERP/MES, Legacy, SDF-based) IIoT-Based Data Integration for Heterogeneous Equipment (Robot, PLC, Vision, Sensor, Gripper) Edge-Native Real-Time Data Integration & Deployment (Edge Computing, Real-time Data Collection) Operations and data monitoring technology |  |  | • Difficulty of standardization of Data structure between the upper system and the field system • Lack of standard interfaces bet. equipment • Complexity of Heterogeneous Equipment connectivity • Difficulty in real-time data synchronization • Lack of data linkage status and history management
Data Layer | [Reality-Virtual Alignment and Calibration] (Step 1) • CAD-Real Scan Data-Based Manual Alignment and Model/Library Construction • Real-Virtual Reference Coordinate Manual Matching & Calibration History Management (Step 2) • Build Sim-Ready Asset Data for Deformed Parts • Automatic alignment and calibration based on reference coordinates and CAD-scan data | [Data Integrity & Digital Consistency Technologies] Integrated Data Management Platform Technology (Data Lake · Data Platform) Digital Twin-linked Digital Asset Management Technology Deformed Part Shape/Physical property Modeling and Sim-Ready Asset Technology integrity Quality Assessment and Verification Technology | [Data Integrity & Digital Consistency Technologies] CAD-Scan Alignment and Reality-Virtual Calibration Technology |  | • Difficulty in maintaining Consistent data integrity across heterogeneous data platforms • Difference in CAD-Actual Shape • Robot/TCP/Vision coordinate mismatch • Difficulty securing precision of ±1 mm or less • Difficulty Maintaining Sim-to-Real Consistency
Decision layer | [AI OLP-based Automatic Robot Teaching and Motion Planning] (Step 1) • Collision avoidance multi-robot trajectory generation and task/sequence optimization (Step 2) • Collaboration sequence/interlock and robot/PLC program automatic generation [Upper-Level Task Planner-Based Multi-Automation Cell Optimization] (Step 2) • Multi-cell Load Distribution and Cycle Time Prediction-based Process Optimization • Human-in-the-loop based plan review and approval (Step 3) • AI Agent-based Autonomous Work Planning and New Cell Auto-Design |  | Motion and Task Planning Technology] Motion/Task Planning and Work Allocation/Sequence Optimization Technology Interlock and Robot/PLC Program Automatic Generation Technology Digital Twin-linked Automatic Teaching Verification and Productivity Analysis Technology Multi-cell integration optimization and layout/robot configuration optimization technology AI Agent-based Autonomous Decision-Making Technology (LLM/VLM-based Support) |  | • Difficulty in generating motion based on complex constraints • Complexity in Multi-cell work allocation and cycle time optimization • Robot teaching automation limits du to Sim-to-Real Gap • Human-in-the-loop based decision-making required

## Slide 10: ③ Autonomous robot teaching and calibration
사내한 (Restricted)
■ Autonomous robot teaching / calibration - Development items / Required technologies / Technical pain points
- Objective : Achieve a "Teaching-less" factory through Digital Twin-based Virtual Commissioning (Sim-to-Real) and establish
an autonomous system that compensates for micro-tolerances of car bodies, parts, and equipment in real-time using edge vision and sensors.
Layer | Development item | Required Skills – DS | Required Skills – Core R&D |  | Development Pain-point
Action Layer | [Closed-loop Control-Based Establishment] (Step 2) • Edge/Sensor-based Real-time Autonomous Precision Control and Feedback Data Collection [Real-time Feedback and Synchronization] (Step 2) • Reflecting field feedback, virtual-real synchronization and trajectory automatic readjustment [Error Detection and Automatic Correction] (Step 2) • Automatic recalibration and replanning, and virtual-real difference correction (Step 3) • Digital Twin / AI Result Field Application and Autonomous Control Enhancement | [Latency Ultra-Low Delay Closed-Loop Technology] Real-time control and communication-based technology (edge-based processing, ultra-low latency real-time communication) Virtual-Real Synchronization & Closed-loop Control Technology Field Application Automation and Deployment/Edge Execution Technology Automatic Recalibration and Adaptive Control Technology | [Real-time Control and Closed-loop Technology] Robot controller integration and force/torque/pressure-based feedback control technology Automatic Recalibration and Adaptive Control Technology |  | • Virtual-Real Robot Response Difference • Gripper force/pressure control difficulty • Environmental change response and automatic recalibration limits • Difficulty in immediately reflecting real-time control errors
Learning layer | [Data Collection and Analysis] (Step 2) • Collect process results, trajectories, and grip state data, and analyze success/failure patterns [Flexible/Deformable Body Learning] (Step 3) • Learn flexible and deformable object behaviors, along with success and failure cases, using Physical AI [AI Agent-based Continuous Learning] (Step 3) • Continuously optimize work sequence, path, and layout • Quality/Maintenance Prediction & Feedback-Based Autonomous Optimization | [AI-based Learning/Distribution/Operation Technology] MLOps-based learning, retraining, & model operation technology AI Agent-based Closed-Loop Learning Architecture Success/Failure case database & Closed-loop learning Technology Digital Twin-Site-Agent Linked Continuous Learning Technology | [AI Self-Learning and Physical AI Technology] Physical AI & Reinforcement learning-based learning technology Success/Failure case database & Closed-loop learning Technology Digital Twin-Site-Agent Linked Continuous Learning Technology [AI Agent Technology] AI Agent-based Closed-Loop Learning Architecture LLM/VLM-based Autonomous Decision-Making and Process Optimization Technology Reinforcement Learning-based Planning · Optimization Technology (RL) |  | • Flexible and deformable body behavior modeling difficulty • Shortage of Rare failure data • Difficulty generalizing learning outcomes to Shop floor • Need to ensure the reliability of AI-generated recommendations and establish a framework for continuous self-optimization

## Slide 11: ③ 로봇 티칭 및 보정 자율화
사내한 (Restricted)
■ 로봇 티칭 및 보정 자율화 - 개발 항목 / 필요 기술 / 극복 과제
- 목표 : 디지털 트윈 기반 가상 시운전 (Sim-to-Real) 으로 로봇 티칭을 제로화 (Teaching-less) 하고, 조립 중 발생하는 차체/부품/설비의
미세 공차를 엣지 비전과 센서로 실시간 자율 보정하는 체계 구축.
계층 | 개발 항목 | 필요 기술 – DS | 필요 기술 – CoreR&D |  | 개발 Pain-point
연결 계층 (Connectivity) | [데이터 인터페이스 및 시스템 연계] (1단계) • 주요 설비 간 연결 체계 및 현장-가상 기초 데이터 연계 구축 • 현장 데이터의 수동·주기적 수집 기반 마련 (2단계) • 현장 운영 데이터 자동 수집·연계 체계 구축 • 현실-가상 데이터 상호 반영을 위한 폐루프 연계 환경 구축 | [통합 연계 플랫폼 기술] • 상위 시스템-현장 데이터 연계 구조 기술 (ERP/MES, Legacy, SDF 기반 연계) • 이기종 설비 API/커넥터 및 IIoT 기반 데이터 연계 기술 (Robot, PLC, 비전, 센서, 그리퍼) • 엣지 기반 실시간 데이터 연계 및 현장 배포 기술 (Edge Computing, 실시간 데이터 수집) • 운영 환경 및 데이터 모니터링 기술 |  |  | • 상위 시스템과 현장 시스템 간 데이터 구조 표준화의 어려움 • 설비 간 표준 인터페이스 부족 • 이기종 설비 연계의 복잡성 • 실시간 데이터 동기화 어려움 • 데이터 연계 상태 및 이력 관리 부족
데이터 계층 (Data) | [현실-가상 정합 및 캘리브레이션] (1단계) • CAD-실물 스캔 데이터 기반 수동 정합 및 모델·라이브러리 구축 • 현실-가상 기준좌표 수동 매칭 및 캘리브레이션 이력 관리 구축 (2단계) • 변형 부품 Sim-Ready 에셋 데이터 구축 • 기준좌표 및 CAD-스캔 데이터 기반 자동 정합 및 캘리브레이션 | [데이터 및 정합 기술] • 통합 데이터 관리 플랫폼 기술 (Data Lake·Data Platform) • 디지털 트윈 연계 디지털 에셋 관리 기술 • CAD-스캔 정합 및 현실-가상 캘리브레이션 기술 • 변형 부품 형상/물성 모델링 및 Sim-Ready 에셋 기술 • 정합 품질 평가 및 검증 기술 |  |  | • 이기종 데이터 플랫폼 간 일관된 데이터 정합 유지의 어려움 • CAD-실물 간 형상 차이 • 로봇/TCP/Vision 좌표 불일치 • ±1 mm 이하 정밀도 확보 어려움 • Sim-to-Real 정합 유지 어려움
의사결정 계층 (Decision) | [AI OLP 기반 자동 로봇 티칭 및 모션플래닝] (1단계) • 충돌회피 멀티 로봇 궤적 생성 및 작업·순서 최적화 (2단계) • 협업 시퀀스·인터락 및 로봇/PLC 프로그램 자동 생성 [상위 레벨 태스크 플래너 기반 멀티 자동화 셀 최적화] (2단계) • 멀티셀 부하 분배·사이클타임 예측 기반 공정 최적화 • Human-in-the-loop 기반 계획 검토 및 승인 (3단계) • AI Agent 기반 자율 작업 계획 및 신규 셀 자동 설계 | [모션·태스크 플래닝 기술] • 모션/태스크 플래닝 및 작업 할당·시퀀스 최적화 기술 • 인터락 및 로봇/PLC 프로그램 자동 생성 기술 • 디지털 트윈 연계 자동 티칭 검증 및 생산성 분석 기술 • 멀티셀 통합 최적화 및 레이아웃/로봇 구성 최적화 기술 • AI Agent 기반 자율 의사결정 기술 (LLM/VLM 기반 지원) |  |  | • 복잡한 제약조건 기반 모션 생성 어려움 • 멀티셀 작업 분배 및 사이클타임 최적화의 복잡성 • Sim-to-Real Gap으로 인한 로봇 티칭 자동화 한계 • Human-in-the-loop 기반 의사결정 필요
조치 계층 (Action) | [폐루프 제어 기반 구축] (2단계) • 엣지·센서 기반 실시간 자율 정밀 제어 및 피드백 데이터 수집 [실시간 피드백 및 동기화] (2단계) • 현장 피드백 반영, 가상-실제 동기화 및 궤적 자동 재조정 [오차 감지 및 자동 보정] (2단계) • 재캘리브레이션·재플래닝 자동 수행 및 가상-실제 차이 보정 (3단계) • 디지털 트윈 / AI 결과 현장 적용 및 자율 제어 고도화 | [실시간 제어 및 폐루프 기술] • 실시간 제어·통신 기반 기술 (엣지 기반 처리, 초저지연 실시간 통신) • 로봇 제어기 연동 및 힘·토크·압력 기반 피드백 제어 기술 • 가상-실제 동기화 및 폐루프 제어 기술 • 현장 적용 자동화 및 배포/엣지 실행 기술 • 자동 재캘리브레이션 및 적응형 제어 기술 |  |  | • 가상-실제 로봇 응답 차이 • 그리퍼 힘/압력 제어 어려움 • 환경 변화 대응 및 자동 재보정 한계 • 실시간 제어 오차의 즉각적 반영 어려움
학습 계층 (Learning) | [데이터 수집 및 분석] (2단계) • 공정 결과·궤적·그립 상태 데이터 수집 및 성공/실패 패턴 분석 [유연체/변형체 학습] (3단계) • Physical AI 기반 유연체/변형체 거동 및 성공/실패 사례 학습 [AI Agent 기반 지속 학습] (3단계) • 작업 순서·경로·배치 지속 최적화 • 품질/유지보수 예측 및 피드백 기반 자율 최적화 | [AI 자기학습 및 Physical AI 기술] • Physical AI 및 강화학습 기반 학습 기술 • 성공/실패 사례 데이터베이스 및 폐루프 학습 기술 • 디지털 트윈-현장-에이전트 연계 지속 학습 기술 • MLOps 기반 학습·재학습·모델 운영 기술 [AI Agent 기술] • AI Agent 기반 폐루프 학습 아키텍처 • LLM/VLM 기반 자율 의사결정 및 공정 최적화 기술 • 강화학습 기반 계획 · 최적화 기술 (RL) |  |  | • 유연체·변형체 거동 모델링 어려움 • 희귀 실패 데이터 부족 • 학습 결과의 생산현장 일반화 어려움 • AI 추천 결과의 신뢰성 확보 및 지속적 자율 최적화 체계 구축 필요
Need to translate KR Ver later

## Slide 12: ④ Autonomous troubleshooting response
사내한 (Restricted)
■ Autonomous response to trouble shooting - Development items / Required technologies / Technical pain points
- Objective : Establish an unmanned maintenance system that identifies root causes in real-time upon equipment failure, autonomously executes
control (PLC) and physical (Humanoid) countermeasures, iteratively retries alternatives until resolved, and self-learns the "Lesson Learned."
Layer | Development Items | Required Technologies - DS | Required Technologies - DX |  | Development Pain-point
Connectivity | [Real-time Fault Detection & Visual Context] Real-time collection of equip. alarms/error codes and integration of high-res vision (CCTV/Robot cameras) from the fault zone [Humanoid Remote/Autonomous Network] Establishing an ultra-low latency communication network with humanoid robots deployed for physical interventions | [Real-time Fault Detection & Visual Context] IIoT sensors and PLC real-time data ingestion. Time-series DB (Influx) collects equipment condition-based monitoring data (i.e. motor speed, variable temperature, vibration etc.) Relational DB (PostgreSQL) for PLC alarm data, process Pack ML state Computer vision and PLC alarms integrated to IoT Platform Computer Vision exposed to MCP Gateway for AI orchestration Use best in class industry standards for PLC protocols, communication (OPC-UA, OPC-UA Companion Specification, and industrial automation standards); Connector and data pipeline to systems /app DB: Production and SAP. Near field camera deployment with visual, video processing capability [Humanoid Remote/Autonomous Network] Establishing wired/wireless ultra-high-speed communication infrastructure for real-time and support Time Sensitive Network (TSN). TSN PLC ready solutions on the edge to support real-time high-speed communication between equipment. Automatic UNS standardization of new equipment including industrial Robotics, autonomous guided vehicles and robotics including Humanoids. | [Real-time Fault Detection & Visual Context] Equipment and process including alarm and equipment state aligns with the Factory process Visual, vision, video to assist in fault identification and trouble shooting [Humanoid Remote/Autonomous Network] Defined Humanoid maintenance / vision related data that is required for ultra-high speed real-time requirements. Humanoid task-based tool selection for key selected maintenance tasks |  | Fragmentation of alarm protocols and error code systems across numerous equipment vendors Non-compliance to standards on PLC equipment process, alarm and tag naming standards. Non-standard protocols used and vendor unique protocols. Vendor locked software code and inability to access equipment alarms, tags and data due to vendor closed system. Securing network bandwidth to transmit humanoid vision data without latency
Data | [Digitization of Maintenance Knowledge & Manuals] Text mining and integrating tens of thousands of pages of P&ID drawings, maintenance manuals, and historical troubleshooting logs [Fault Context Synchronization] Providing AI with a synchronized timeline combining maintenance manuals and time-series data (temperature, vibration, pressure) at the exact moment of the error code | [Digitization of Maintenance Knowledge & Manuals] Rapid ingestion of multi-lingual equipment manuals, breakdown-reports. Data ingestion of complex engineering drawings (e.g. EPlan) including mechanical, electrical and engineering workflow SoPs. Enterprise level Master Data Management and process standardization across all Supply Chain pillars (maintenance, production, quality, logistics) Data streaming, pipelines and data platform towards data product creation for advanced use-cases such as analytics and AI/ML etc). [Fault Context Synchronization] Time stamp data synchronization and real-time agents at edge to drive real-time root cause analysis and prescriptive self-learning for maintenance efficiency. | [Digitization of Maintenance Knowledge & Manuals] Document repository with version control Human-constructed SoPs in place aligned to the factory process, standardized, contextualized and updated. [Fault Context Synchronization] Data source is contextualized and seamless connectivity to IIoT Platform |  | Extremely low data quality of past maintenance logs, often written in unstructured text or handwriting by workers Unstructured breakdown report and quality of RCA and diagnosis Different equipment and core systems Technical difficulty in converting complex drawings and manuals into vector formats understandable by AI

## Slide 13: ④ Autonomous troubleshooting response
사내한 (Restricted)
■ Autonomous response to trouble shooting - Development items / Required technologies / Technical pain points
- Objective : Establish an unmanned maintenance system that identifies root causes in real-time upon equipment failure, autonomously executes
control (PLC) and physical (Humanoid) countermeasures, iteratively retries alternatives until resolved, and self-learns the "Lesson Learned."
Layer | Development Items | Required Technologies - DS | Required Technologies - DX |  | Development Pain-point
Decision | [Root Cause Analysis (RCA)] Knowledge Graph-based fault cause diagnosis and prediction by synthesizing error codes, equipment-generated data, and vision images (e.g., accurately diagnosing PLC/Robot logic errors, sensor false detections, failures, and mechanical jamming) [Multi-modal Countermeasure Generation & Iterative Logic] ① 1st Action: Proposing improvement logic and automatic correction for faulty programs ② 2nd Action (1st fail): Dispatch humanoid to remove jammed part (H/W action) [Safety & Interference Validation] Pre-verifying power lockout (LOTO) and collision risks with other equipment using a rule engine and digital twin before humanoid deployment | [Root Cause Analysis (RCA)] • Knowledge Graph: Mapping Symptom ➔ Cause ➔ Action • Generative AI (RAG), Agentic AI [Multi-modal Countermeasure Generation & Iterative Logic] • Knowledge graph and LLM for PLC programs • Digital Twin action-to-effect prediction before execution [Safety & Interference Validation] • Digital Twin collision and interference simulation • Virtual PLC sandbox for pre-execution verification | [Root Cause Analysis (RCA)] • Standardized fault-code master across equipment vendors • SAP PM breakdown history restructured for RCA consumption • Diagnostic result UI with evidence presentation for PIC [Multi-modal Countermeasure Generation & Iterative Logic] • HITL approval workflow and authority matrix • PLC change control: version, approval, rollback, audit log • Auto work-order issuance and parts reservation to SAP [Safety & Interference Validation] • Digitized LOTO permit integrated with EHS • Safety zone and access control |  | • Controlling Hallucination where Generative AI misinterprets manuals and issues incorrect re pair instructions • Complexity of the Dynamic Decision Tree required to roll back to the previous state and find new alternatives if an action fails
Action | [S/W Autonomous Control Action] Resolving logic errors and Autonomously changing process conditions by transmitting direct reset commands or parameter and recipe updates to the equipment PLC through IoT platforms and edge controllers [H/W Physical Autonomous Action] Performing physical maintenance, such as moving a humanoid robot to the site to clear jams and replace faulty parts during component jamming or failure troubleshooting" | [H/W Physical Autonomous Action] • Virtual PLC and edge computing [H/W Physical Autonomous Action] • Near field GPU processing with high computation power | [S/W Autonomous Control Action] • Core system orchestration to drive closed loop control action between IoT and PLC. [H/W Physical Autonomous Action] • Autonomous task-based Force & Torque Compliance Control • Task coordinated vision guided manipulation |  | • Extreme difficulty in humanoid manipulation requiring unstructured and delicate force, such as extracting tightly jammed parts or connecting fine wires
Learning | [Autonomous Lesson Learned Generation] Upon successful troubleshooting, automatically updating the Knowledge Graph with a new node detailing "which action was effective for which symptom" [Humanoid Skill Reinforcement Learning] If a humanoid succeeds after multiple failed attempts to extract a part, the AI uses reinforcement learning on that successful force and trajectory to improve future success rates | [Autonomous Lesson Learned Generation] • KG auto-update pipeline: symptom → cause → action → outcome nodes • MLOps: continuous diagnostic model retraining [Humanoid Skill Reinforcement Learning] • Reinforcement Learning (Humanoid physical skill learning) • MLOps: robot control model redeployment to edge | [Autonomous Lesson Learned Generation] • Lesson Learned repository with automatic SOP update that can include visual, video captured • Structured outcome capture at work order closure [Humanoid Skill Reinforcement Learning] • Skill library registry and version management • Task catalogue of autonomy-eligible maintenance tasks |  | • Lack of technology to extract the humanoid’s physical success experience (force, angle, friction) into quantitative data and transfer it into AI model weights (Skill Transfer)

## Slide 14: ④ 트러블 슈팅 대응 자율화
사내한 (Restricted)
■ 트러블 슈팅 대응 자율화 - 개발 항목 / 필요 기술 / 극복 과제
- 목표 : 설비 장애 발생 시 실시간으로 원인을 규명하고, 제어 (PLC) 및 물리적 (휴머노이드) 조치를 자율적으로 수행하며,
해결될 때까지 대안을 반복 실행한 후 레슨런 (Lesson Learned) 을 스스로 학습하는 무인 정비 체계 구축.
계층 | 개발 항목 | 필요 기술 – DS | 필요 기술 – DX |  | 개발 Pain-point
연결 계층 (Connectivity) | [실시간 장애 인지 및 현장 시야 확보] 설비의 알람/에러 코드 실시간 수집 및 장애 발생 구역의 고해상도 비전(CCTV/로봇 카메라) 데이터 연동 [휴머노이드 원격/자율 제어망] 물리적 조치를 위해 투입되는 휴머노이드 로봇과의 초저지연 통신망 개통 | • IIoT 플랫폼 (현장 데이터 실시간 수집) • AI Smart Vision (장애 상황 시각적 인지) • 무선 / 유선 초고속 통신 인프라 구축 • 오픈소스 표준 데이터 프로코톨 제정 |  |  | • 수많은 설비 제조사(Vendor)마다 각기 다른 알람 프로토콜과 에러 코드 체계의 파편화 • 휴머노이드의 시야(Vision) 데이터를 지연 없이 전송하기 위한 대역폭 확보
데이터 계층 (Data) | [정비 지식 및 매뉴얼 데이터화] 수만 페이지에 달하는 설비 도면(P&ID), 정비 매뉴얼, 과거 작업자의 트러블 슈팅 이력(Log)을 텍스트 마이닝하여 통합 [장애 컨텍스트(Context) 동기화] 에러 코드 발생 시점의 설비 온도, 진동, 압력 등 시계열 데이터와 정비 매뉴얼을 하나의 타임라인으로 묶어 AI에 제공 | • Text Mining / OCR (비정형 문서 데이터화) • 시계열 Database 및 AI 모델 (시간 흐름 기반 영상 + 텍스트 통합) • SDM (설비 기준 정보 및 부품 BOM 관리) |  |  | • 과거 정비 이력이 작업자의 수기나 비표준화된 텍스트로 작성되어 있어 데이터의 품질(Quality)이 매우 낮음 • 복잡한 도면과 매뉴얼을 AI가 이해할 수 있는 벡터(Vector) 형태로 변환하는 기술적 난이도
의사결정 계층 (Decision) | [근본 원인 분석 (RCA)] 에러 코드와 설비 생성 데이터, 비전 이미지 종합하여 Knowledge Graph 기반의 고장 원인 진단, 예측 (예: PLC / Robot 논리 오류, 센서 오감지, 고장, 기계적 고착 등을 정확히 진단) [다중 모달 대책 생성 및 반복 로직] ① 1차 대책: 오류 프로그램에 대한 개선 로직 제안 및 자동 수정 ② 2차 대책 (1차 실패 시): 휴머노이드 투입 및 부품 탈거 (H/W 조치) [안전 및 간섭 검증] 휴머노이드 투입 전, 해당 구역의 전원 차단(LOTO) 여부 및 타 설비와의 충돌 가능성을 규칙 엔진과 디지털 트윈으로 사전 검증 | • Diagnostic AI: 근본 원인 분석 (RCA) • Generative AI (RAG): 매뉴얼 기반 조치 순서(Step) 자동 생성 • Knowledge Graph: 증상 ➔ 원인 ➔ 조치 매핑 • Rule Engine: 정비 안전 수칙(LOTO 등) 강제 |  |  | • 생성형 AI가 매뉴얼을 잘못 해석하여 엉뚱한 정비 지시를 내리는 환각(Hallucination) 현상 통제 • 조치 실패 시, 이전 상태로 롤백(Roll-back)하고 새로운 대안을 찾는 동적 의사결정 트리 (Dynamic Decision Tree)의 복잡성
조치 계층 (Action) | [S/W 자율 제어 조치] IoT 플랫폼과 엣지 컨트롤러를 통해 설비 PLC에 직접 리셋 명령이나 파라미터 및 레서피 변경값을 전송하여 논리 오류 해결 및 공정조건 자율변경 [H/W 물리적 자율 조치] 부품 끼임(Jamming)이나 고장 조치 시, 휴머노이드 로봇이 현장으로 이동하여 끼임 제거 및 이상 부품 교체 등의 물리적 정비 수행 | • Virtual PLC 및 엣지 컴퓨팅 • Humanoid Robotics (비정형 물리적 정비) • Vision-AI Guided Manipulation (시각 기반 조작) • Force & Torque Compliance Control (부품 파손 방지 힘 제어) |  |  | • 꽉 끼인 부품을 빼내거나 미세한 선을 연결하는 등, 비정형적이고 섬세한 힘(Force)이 요구되는 휴머노이드 조작(Manipulation)의 극단적 난이도
학습 계층 (Learning) | [레슨런(Lesson Learned) 자율 생성] 트러블 슈팅이 최종 성공하면, "어떤 증상에 어떤 조치가 유효했는지"를 지식 그래프에 새로운 노드(Node)로 자동 업데이트 [휴머노이드 스킬 강화학습] 휴머노이드가 부품을 빼내는 데 여러 번 실패하다 성공한 경우, 그 성공적인 힘의 조절과 궤적을 AI가 강화학습하여 다음 정비 시 성공률 향상 | • Knowledge Graph Auto-updating (지식 자동 확장) • Reinforcement Learning (휴머노이드 물리 스킬 학습) • MLOps (진단 모델 및 로봇 제어 모델 재배포) |  |  | • 휴머노이드의 물리적 성공 경험(힘, 각도, 마찰력)을 정량적 데이터로 추출하여 AI 모델의 가중치로 변환(Skill Transfer)하는 기술의 부재
Need to translate KR Ver later

## Slide 15: ⑤ Autonomous quality defect analysis and response
사내한 (Restricted)
■ Autonomous quality defect cause analysis and response - Development items / Required technologies / Technical pain points
- Objective : Establish an unmanned quality control system that integrates data from VDR inbound, logistic to final assembly,
autonomously diagnosing root causes (Part/Logistic/Equipment/Worker) of defects, and executing actions such as equipment parameter correction
and automated engineering ticket issuance.
Layer | Development Items | Required Technologies – DS | Required Technologies – DX |  | Development Pain-point
Connectivity | [End-to-End Core Quality Data Collection by Process] Supplier Incoming Items: Lot tracking data, inspection data, transportation environment monitoring Body : Body quality data such as BIW frame accuracy, welding data, gap/step data, etc. Paint : Paint quality data such as film thickness, clearance, etc. Assembly: Fastening torque, gap & flush, driving, BSR (Buzz, Squeak, Rattle), water tightness, interior/exterior inspection result data [Market Quality Data] Real-time integration of field data | [S/W] IIoT Middleware Layer MQTT Broker for lightweight IoT devices Kafka-based event streaming (or equivalent) Time-series DB connector (InfluxDB, Timescale) Q-DB Connector MCP Gateway [H/W] Real-time Data Streaming Backbone Low-latency network (10 Gbps minimum for vision data) Edge Computing Node (for real-time vision processing) Optical/Vision: Inline 3D Scanner, High-res Machine Vision, 3D Laser Profiler Precision Measurement : CMM (Coordinate Measuring Machine - Press/Inbound), Ultrasonic NDT (Non-Destructive Testing - Body Weld), Coating Thickness Gauge (Paint), Smart Torque Wrench Plant Track and Trace solution: RFID/Barcode Scanner, High-perform. | [End-to-End Core Quality Data Collection by Process] Incoming part quality checks Items: Part traceability Press: Mold condition monitoring, press pressure/temperature/vibration/shape measurement Body-in-White (BIW): BIW dimensional accuracy, welding data, robot position data, gap/step Paint: Coating thickness, clearance, painting environment data, cleanliness/temperature/humidity data Assembly: Fastening torque, gap & flush, driving, BSR (Buzz, Squeak, Rattle), water tightness, interior/exterior inspection result data Market Quality Data - Real-time integration of field data |  | Limitations in digitizing and integrating inbound inspection certificates from numerous VDRs Inconsistent data formats across suppliers, lack of data reliability Increased data complexity due to multiple vehicle models and options Requirement for processing large-scale real-time data
Data | [Establishing VIN-Based Digital Thread] Data integration across connection layers by VIN (Integrating process data into vehicle-unit quality data) - Critical quality process parameters -> SPC (CPK) (Within work instruction) - FMEA - Field claims - Q-DB (Global Counter measure, root causes ..etc) [Metrics Definition] - Monitoring Critical quality process - Monitoring KPI target metrics [Quality Data Standardization] Requirement for standard coding of defect information data for each process | Single Data Model to support VIN-Based Digital Thread and track and trace - Knowledge Graph Master Data Management (MDM) & Data standardization for Quality Unified defect classification (VDR, Press, BIW, Paint, Assembly, Market) Equipment master data (capability, calibration status) BOM, Production plan, Car, Work order, etc.. Process specification database (tolerance, parts, quality process parameters, equipment) Data Lakehouse | [Establishing VIN-Based Digital Thread] Data integration across connection layers by VIN (Integrating process data into vehicle unit quality data) Critical quality process parameters -> SPC (CPK) (Within work instruction) FMEA Field claims Q-DB (Global Counter measure, root causes ..etc) [Metrics Definition] Monitoring Critical quality process Monitoring KPI target metrics |  | Non-standardization of quality data structures Data disconnection / data loss between processes Securing sufficient data related to quality defects and their causes

## Slide 16: ⑤ Autonomous quality defect analysis and response
사내한 (Restricted)
■ Autonomous quality defect cause analysis and response - Development items / Required technologies / Technical pain points
- Objective : Establish an unmanned quality control system that integrates data from VDR inbound, logistic to final assembly,
autonomously diagnosing root causes (Part/Logistic/Equipment/Worker) of defects, and executing actions such as equipment parameter correction
and automated engineering ticket issuance.
Layer | Development Items | Required Technologies – DS | Required Technologies – DX |  | Development Pain-point
Decision | [Multivariate Root Cause Analysis (RCA)] In the event of a defect, AI traces back the real cause among the 5 major factors (e.g., "Assembly Gap defect = 70% Moving mounting error 70% + 30% Body welding distortion") (FMEA + Field) [Cause-specific Autonomous Countermeasure Generation] ① Equipment / worker issue : Calculation of correction values ​​ for moving mounting robots, countermeasures for worker assembly defects, etc. ② Part: Hold usage of the VDR Lot | Production/Quality Knowledge Graph: Mapping Defect ➔ Cause ➔ Action Kafka (Event streaming) QMS / MES Integration OPC UA/ MQTT Integration for equipment AI Agent (Real-time parameter control) Anomaly Detection Engine Root Cause Correlation Engine Confidence Scoring & Evidence Ranking Multivariate correlation analysis (RCA) Complex Event Processing (CEP) | [Multivariate Quality RCA with HITL Validation] For a quality defect, AI traces back the real cause among the 5 major factors (e.g., "Assembly Gap defect = 70% Press outer panel dimension error + 30% Body welding distortion") -> General recommendation verified by SME [Real-Time Anomaly Detection & Early Warning] Baseline Quality Anomaly Detection: establish statistical baselines and detect anomalies in real-time Predictive Defect Probability Scoring : Score incoming products with defect risk before they move to next process [Root Cause Correlation Engine] Cross-Process Correlation Analysis: Map defects detected in Assembly back to Press, BIW, Paint stages using VIN traceability |  | • Limitations of AI clearly identifying the cause of defects • Possibility of errors in countermeasures when the causes of quality defects are complex • Model consistency when training data on quality defects and causes is insufficient
Action | [Autonomous Equipment Parameter Correction] Automatically reflecting AI-derived offset values into press pressure, welding robot trajectory, and painting robot injection amount in real-time via edge controllers (S/W Action) [Autonomous Production Part Control] If the cause is an inbound part, integrating with WMS/MES to immediately block the Lot from entering the line and auto-sending a Quality Claim to the VDR [Automated Engineering Ticket Issuance] If a quality issue is determined to be due to worker non-compliance with standards, a work order (Ticket) is automatically issued to the site manager with an attached 'RCA Report'. | Production/Quality Knowledge Graph: Mapping Defect ➔ Cause ➔ Action Kafka (Event streaming) QMS / MES Integration OPC UA/ MQTT Integration for equipment AI Agent (Real-time parameter control) AI Agent (Automated ticket issuance) Anomaly Detection Engine Root Cause Correlation Engine Confidence Scoring & Evidence Ranking Multivariate correlation analysis (RCA) Complex Event Processing (CEP) | [Quality Containment & Production RCA Automation] ① Equipment / worker issue : Calculate offset values for robot sealing trajectory, Worker assembly defects, etc ② Part: Hold usage of the VDR Lot (Part block) [Adaptive Equipment Parameter Correction] Automatically reflecting AI-derived offset values into sealing robot trajectory etc in real-time via edge controllers (S/W Action) [Autonomous Production Part Quality Control] If the cause is an inbound part, integrating with WMS/MES to immediately block the Lot from entering the line and auto-sending a Quality Claim to the vendor [Adaptive Response Prioritization] Cost-Benefit Analysis for Corrective Actions. Dynamic Resource Allocation |  | • Liability issues regarding safety accidents and massive line-stop risks that may occur when AI autonomously changes equipment parameters • Potential contractual/legal disputes when automatically issuing claims to VDRs

## Slide 17: ⑤ Autonomous quality defect analysis and response
사내한 (Restricted)
■ Autonomous quality defect cause analysis and response - Development items / Required technologies / Technical pain points
- Objective : Establish an unmanned quality control system that integrates data from VDR inbound, logistic to final assembly,
autonomously diagnosing root causes (Part/Logistic/Equipment/Worker) of defects, and executing actions such as equipment parameter correction
and automated engineering ticket issuance.
Layer | Development Items | Required Technologies – DS | Required Technologies – DX |  | Development Pain-point
Learning | [Autonomous Quality Knowledge Graph Expansion] Automatically adding new causal nodes (e.g., "Part A dimension error + Weld Temp B = Gap Defect C") to the Knowledge Graph when new defect types and solutions are confirmed [Evolution from Reactive to Predictive Quality] Based on accumulated RCA data, it has been retrained into a preventive model that warns of "expected watertightness failures during assembly line" by detecting only minute changes in paint sealing quality. | MLOps Pipelines: (continuous model deployment/Mgm.) Predictive Quality Model KG Ontology Schema Registry | [RCA Outcomes Capture] KG enrichments based on learnings from RCA [Evolution from Reactive to Predictive Quality] Retraining the model based on accumulated RCA data to warn, "Watertightness defect expected during Assembly," just by observing micro-dimension changes in the Press process [AI Explainability & Confidence Scoring] Root Cause Confidence Ranking. Explanation Generation for Corrective Actions |  | The Delayed Feedback Loop problem: If a gap /flush defect found in Assembly originated in Body line, the time gap makes it difficult for AI to learn immediate rewards

## Slide 18: ⑤ 품질 불량 원인 분석 및 조치 자율화
사내한 (Restricted)
■ 품질 불량 원인 분석 및 조치 자율화 - 개발 항목 / 필요 기술 / 극복 과제
- 목표 : VDR 부품 입고부터 물류/의장 라인 전체의 품질 데이터를 통합하여, 불량 발생 시 근본 원인 (부품/물류/설비/작업자) 을 자율 진단하고,
최적의 대책을 실행하는 무인 품질 관제 체계 구축.
계층 | 개발 항목 | 필요 기술 – DS | 필요 기술 – DX |  | 개발 Pain-point
연결 계층 (Connectivity) | [End-to-End 공정별 핵심 품질 데이터 수집] • 협력사 입고품 : 로트 추적 데이터, 검사데이터, 운송 환경 모니터링 • 차체: BIW 골격 정도, 용접 데이터, 갭/단차 데이터 등 차체 품질 데이터 • 도장: 도막 두께, 클리어런스 등 도장 품질 데이터 • 의장: 체결 토크, 갭/단차(Gap & Flush), 주행, BSR, 수밀, 내/외관 검사 결과 데이터 [시장품질 데이터] 필드 데이터 실시간 연동 | [S/W] IIoT 플랫폼, 고속 데이터 수집 파이프 라인 [H/W] • 광학/비전: 인라인 3D 스캐너, 고해상도 머신 비전, 3D 레이저 프로파일러 • 정밀 계측기: 3차원 측정기(CMM), 초음파 비파괴 검사기(NDT- 차체 용접), 도막 두께 측정기(도장), 스마트 토크 렌치(의장) • 추적/수집 : RFID/바코드 스캐너, 대용량 비전 처리용 고성능 Edge Gateway (IPC) |  |  | • 수많은 VDR의 입고 검사 성적서 디지털화 연동 한계 • 협력사별 데이터 포맷 불일치, 데이터 신뢰성 부족 • 다차종/다옵션에 따른 데이터 복잡성 증가 • 대용량 실시간 데이터 처리 필요
데이터 계층 (Data) | [VIN 기반 디지털 스레드 구축] VIN별 연결 계층의 데이터 통합 (공정데이터를 차량 단위 품질 데이터로 통합) [품질 데이터 표준화] 각 공정별 불량 정보 데이터의 표준 코드화 필요 | • Data Lakehouse (시계열 + 3D/이미지 통합) • Data Genealogy / Traceability System • MDM (품질 불량 코드 표준화) |  |  | • 품질 데이터 구조의 비표준화 • 공정간 데이터 단절 / 누락 • 품질 불량 및 원인과 관련된 충분한 데이터 확보
의사결정 계층 (Decision) | [다변량 근본 원인 분석 (RCA)] 불량 발생 시 5대 요인 중 진짜 원인을 AI가 역추적 (예: "의장 단차 불량 원인 = 무빙 장착 오차 70% + 차체 용접 변형 30%") [원인별 맞춤형 대책 자율 수립] ① 설비/작업자 원인 : 무빙 장착 로봇 보정치 계산, 작업자 조립 불량 대책 등 ② 부품 원인 : 해당 VDR 로트(Lot) 라인 투입 보류 판정 [디지털 트윈 검증] AI가 계산한 보정값을 가상 공정에 적용하여 2차 불량 (Side-effect) 발생 여부 사전 검증 | • Diagnostic AI: 다변량 상관관계 분석 (RCA) • Knowledge Graph: 불량 증상 ➔ 원인 ➔ 대책 매핑 • Digital Twin: 3D 공차 분석 • Generative AI: 불량 분석 리포트 자동 생성 |  |  | • 불량의 원인이 무엇인지 AI 가 명확히 구분해 내는 것의 한계 • 품질 불량의 원인이 복합적일 경우, 대책 오류의 가능성 • 품질 불량 및 원인 학습 데이터가 부족할 경우 모델 정합성 부족
조치 계층 (Action) | [설비 파라미터 자율 보정] AI가 도출한 보정값을 엣지 컨트롤러를 통해, 차체 용접 조건 등에 실시간 자동 반영 (S/W 조치) [VDR 부품 자율 통제] 불량 원인이 입고 부품일 경우, WMS/MES와 연동하여 해당 로트의 투입을 즉시 차단하고 VDR에 품질 클레임 자동 발송 [엔지니어링 티켓 자동 발행 (작업자)] 품질 문제가 작업자 표준 미준수로 판명될 경우, 자율적으로 현장 관리자에게 'RCA 리포트'를 첨부하여 작업 지시서(Ticket) 자동 발행 | • Edge Computing (설비 파라미터 실시간 제어) • QMS / MES Integration (품질/제조 실행 연동) • RPA (VDR 클레임 및 티켓 발행 자동화) |  |  | • AI가 설비 파라미터를 자율적으로 변경했을 때 발생할 수 있는 안전사고 및 대규모 라인 정지 리스크에 대한 책임 소재 • VDR에 대한 자동 클레임 발행 시 발생하는 계약적/법적 분쟁 소지
학습 계층 (Learning) | [품질 지식 그래프 자율 확장] 새로운 유형의 불량과 그 해결책이 확인되면, 지식 그래프에 "A부품 치수 오차 + B용접 온도 = C단차 발생"이라는 새로운 인과관계 노드 자동 추가 [사후 분석에서 예방 품질로 진화] 축적된 RCA 데이터를 바탕으로, 도장 실링 품질의 미세한 변화만 보고도 "의장 라인 조립 시 수밀 불량 발생 예상"을 경고하는 예방 모델로 재학습 | • Knowledge Graph Auto-updating • MLOps (품질 예측 모델 지속 배포 및 모니터링) • Explainable AI (XAI) (엔지니어 설득용 근거 시각화) |  |  | • 의장 라인에서 발견된 갭/단차 불량의 원인이 차체 라인에 있을 경우, 피드백 루프가 너무 길어 AI가 즉각적인 보상을 학습하기 어려운 문제
Need to translate KR Ver later

## Slide 19: ⑥ EHS
사내한 (Restricted)
■ Autonomous response to trouble shooting - Development items / Required technologies / Technical pain points
- Objective : Establish an unmanned maintenance system that identifies root causes in real-time upon equipment failure, autonomously executes
control (PLC) and physical (Humanoid) countermeasures, iteratively retries alternatives until resolved, and self-learns the "Lesson Learned."
Layer | Development Items | Required Technologies - DS | Required Technologies - DX
Connectivity | [In-line Energy Consumption Management] Monitor of energy consumption in DT [Fire hazard detection] Monitoring of fire hazards in DT | Real time event streaming through Kafka​ IIoT: Data Ingestion from sensors, PLC, etc.​ Investment of thermal cameras and required sensors Time-series DB (influx) to support massive data ingestion sensors and equipment readings​ Event streaming (Kafka) for real time event and alerts​ NoSQL for unstructured data​ Data platform to enable ETL, analysis and development of data products​ | 
Data | [Digital Twin –Factory Facility Management] Prepare DT platform to model real-life operations by preparing connectivity, data and 1D /2D / 3D assets [Traffic safety monitoring and management] Real-time integration and monitoring of AMR / AGV / parking robot traffic | Need Data Platform to facilitate the creation of “data products” to enable daily advanced analytics, as well as advanced use-cases (AI/ML etc)​ SDM : Facility , Mobile Robot SIM: Omniverse, OpenUSD, Metropolis​ Mobile robot telemetry​ Data retention, archival and housekeeping policy OPC UA/ MQTT Integration for equipment safety​ Integration with MES and ERP for production / customer data | Real-time monitoring of status of AMR / AGV / parking robot, with easy access to contextual information for further analysis
Decision | [Safety incident response with integration with mobile robot team] Autonomous decision making for incident response and coordination with mobile robot team [Integration with planning team for energy and safety issues] Energy optimization, mobile robot route to alert production planning on production impact [Fire incident response and integration with planning team] Autonomous decision making based on identified fire hazard and integration with planning team on capacity impact | Kafka (Event Streaming)​ MCP Gateway ​ Edge Computing Nodes (Private 5G-connected)​ Digital Twin Integration - State Reader, Floor Topology​ Audit Log​ Simulation and optimization decision engines Integration to MES / factory activities | Facility digital model replicating activities, properties and behaviours in real-world Path planning and conflict resolution Dynamic load balancing for electrical supply Dynamic mission control with critical fire-fighting equipment and other mission-critical equipment Managers can compare expected effects (KPI changes) by scenario. Governed approval UI for AI recommendations.​ Integration with other application areas e.g. Production Planning, Logistics, Maintenance
Action | [Reusable Energy Management] Connection with solar energy management system and link with production planning | Kafka (Event Streaming) MCP Gateway Edge Computing Nodes (Private 5G-connected) OPC UA/ MQTT Integration for dynamic mission control | Path planning and conflict resolution Integration with other application areas e.g. Production Planning, Logistics, Maintenance Dynamic mission control with waste disposal systems
Learning | Performance monitoring of AI model use and DT simulation | • MLOps Pipelines: (continuous model deployment/Mgm.) • Hi-Fidelity Event Log: ‘Black Box’ recorder • State-Action mapping engines • Contextual Metadata Tagging |